## Slide 1: ENCE 231: Engineering Geology Fall Semester 2017/2018 Department of Civil Engineering- Birzeit University, Palestine Chapter 2: Minerals
Instructor: Saheem

## Slide 2: Minerals: Source of Manufactured Products
Minerals are the source of every manufactured product.
Known examples: aluminum in food or beverage cans, copper in wiring, gold & silver in jewelry, etc…
Other not so known examples: graphite in lead pencils, talc in shower products, diamonds in drill bits at dentist, quartz a source of silicon for computer chips, etc…
There are more around 4,000 minerals on earth… defined so far…

## Slide 3: Minerals: Definition & Characteristic
The term “mineral” is used in different ways:
In Sports & Fitness: concerned with vitamins & minerals.
Mining Industry: minerals are anything extracted from the ground (ex: coal, iron ore, sand and gravel, etc.)
The definition in Geology: “Any naturally occurring inorganic solid that possesses an orderly crystalline structure and a definite chemical composition.”
Mineral Characteristics:
Naturally Occurring.
Solid Substances.
Orderly Crystalline Structure.
Definite Chemical Composition.
Generally Inorganic.

## Slide 4: Minerals: Building Blocks of Rocks
A Rock is a solid mass composed of one or more minerals combined in some form.
Monomineralic Rocks: rocks almost entirely composed of one mineral (ex: limestone  calcite, salt  halite ).
Polymineralic Rocks: consists of several minerals (ex: granite has several minerals in aggregate form).
However, some rocks are composed of non-mineral matter (ex: obsidian, pumice, coal).

## Slide 5: Minerals: Elements, Atoms, & Chemical Bonding
Protons (+)= electrons (-)
What makes up an atom?

## Slide 6: Minerals: Why Atoms Bond
Principle Shells: Valence electrons are the electrons in the outermost shell in an atom. The number of valence electrons determines its stability & whether the atom will bond with other atoms.
Ionic Bond: when electrons are transferred.
Covalent Bond: electrons are shared.

## Slide 7: Minerals: Isotopes & Radioactive Decay
Atoms of the same element have the same number of protons, but may have a different number of neutrons (isotopes of the element).

## Slide 8: Minerals: Isotopes & Radioactive Decay (C-14 Dating/ Radioactive Dating)

## Slide 9: Properties of Minerals
Each Mineral has a definite chemical composition and orderly arrangement of atoms, which gives it a unique set of physical properties.
Primary Physical Properties used to identify minerals:
Crystal Form
Luster
Color
Streak
Hardness
Cleavage
Density & Specific Gravity
Secondary Properties: magnetism, taste, feel, smell, elasticity, malleability, double refraction, & chemical reaction to hydrochloric acid (HCl).

## Slide 10: Primary Physical Properties: 1) Crystal Form
The Crystal Form reflects the internal orderly arrangements of atoms in a particular mineral.
When enough space & time are available to the mineral, its crystal faces will form well.
When space & time are NOT Available, the result is an intergrown mass of small, jammed crystals that are not clearly visible to the unaided eye.
Quartz
Well Formed Hexagonal crystal
Granite Intergrown minerals

## Slide 11: Primary Physical Properties: 2) Luster
Luster is the appearance or quality of light reflected from the surface of a mineral.
Minerals that have the appearance of metals are described as having a “Metallic Luster”.
Other non-metallic luster include: Vitreous or Glassy (such as quartz), pearly, silky, resinous, and earthy (dull).
Hematite
Metallic Luster
Galena
Metallic Luster
Dolomite
Dull, Non-metallic Luster

## Slide 13: Primary Physical Properties: 3) Color
Color is NOT a reliable diagnostic property, but may help in certain cases.
Quartz in Variable Colors

## Slide 14: Primary Physical Properties: 4) Streak
Streak is the color of a mineral in its powdered form, which is much more reliable. A mineral in different colors will have the same color streak.

## Slide 15: Primary Physical Properties: 5) Hardness
Hardness is one of the most useful diagnostic properties. It is a measure of the resistance of a mineral to abrasion or scratching. It is determined by rubbing it with another mineral of known hardness.
Mohs Hardness Scale:
A scale from 1 (softest) to 10 (hardest).
Example of Gypsum & Calcite.

## Slide 16: Primary Physical Properties: 6) Cleavage
Cleavage:
Depending on the chemical bonding, a mineral will break along the weak bonds when it is stressed. The planes it breaks along are called “Cleavage Planes”. They appear as smooth surfaces with the same geometry when breakage occurs.

## Slide 17: Primary Physical Properties: 6) Cleavage
Cleavage:
Minerals may cleave along 1, 2, 3 or more planes. If more than 1, we describe the angle between the different cleavage planes
However, this is not to be confused with crystal faces!
Some mineral will not cleave but may break into pieces that do resemble each other (Ex: Quartz and Conchoidal Fracturing)

## Slide 18: Primary Physical Properties: 6) Density & Specific Gravity
Density is an important property in defining matter, including minerals, that is expressed in grams/cubic centimeter (g/cm3).
Specific Gravity (unitless) is used in place of density as it is easier to find or estimate. It compares the weight of a mineral compared to the same volume of water.
Rock-forming minerals that weigh similar to common rocks, we estimate that it has a Specific gravity of 2.5-3.
Some metallic minerals weigh much more than common rock (ex: Galena Sg= 7 , or pure 24-kurot gold =20 or so)

## Slide 19: Mineral Groups
There are nearly 4,000 mineral, but only a few dozen are abundant. They are the “Rock-Forming Minerals”.
Only 8 elements make up the bulk of these minerals and represent 98% of the continental crust (by weight).
The elements are:
Oxygen (O) [46%] & Silicon (Si) [27.7%] combine together to form the most abundant mineral group, the Silicates.
Other Elements: Aluminum (Al), Iron (Fe), Calcium (Ca), Sodium (Na), Potassium (K), & Magnesium (Mg).

## Slide 20: Mineral Groups: Silicates
Silicate minerals make up 90% of the Earth’s crust. They occur when Silicon & Oxygen bond (covalent) to form the Silicon-oxygen tetrehedron (SiO4¯⁴).
“Tetra-” is derived from ancient Greek meaning “four”. This signifies the structure of ionic bonding (i.e. four Si⁺⁴ ions per O⁻2).
These tetrahedra are not chemical compounds, but rather complex ions having a net charge of (-4). To become electrically balanced/ neutral, these complex ions bond to other positively charged elements such as Mg, Ca, Fe, K, Na, K, etc.
Mg or Fe bond with the outer oxygens to form a single tetrahedron  the mineral Olivine

## Slide 21: Silicate Structures
Other than bonding with positive ions, the tertahedra may link with themselves in a variety of ways (through sharing of oxygen), forming: single chain, double chain, sheet, & 3-D network structures.

## Slide 22
So, in each of the silicate structures the ratio of oxygen ions to silicon ions differs.
Consequently, as more of the oxygen ions are shared, the % of silicon increases. Therefore, silicates are described as either having “high” or “low” silicon content.
O:Si
4: 1
O:Si
3:1
O: Si
2:1

## Slide 23: Example Silicates
Ions with approx. the same size & charge are able to substitute freely for one another. Example: Fe+2 and Mg+2 can substitute without changing the mineral crystal structure (see Olivine).
Note that Aluminum also often substitutes for the Silicon in the silicon-oxygen tetrahedron!!!

## Slide 24: Common Silicate Minerals
We now know that the building block for silicates is SiO4¯⁴. Each group of silicates has a particular structure & because Si-O bond are strong covalent bonds, the silicate mineral tend to cleave (break) between the Si-O bond rather than across them.
Feldspar Group (Orthoclase, Plagioclase):
Most abundant silicate (comprising 50% of earth’s crust).
Quartz:
Second most abundant silicate & the only common mineral made up completely of silicon and oxygen (SiO2).

## Slide 25: Other Common Silicates
Mica: Biotite, Muscovite
Amphibol (Hornblend)
Pyroxene (Augite)
Olivine
Biotite
Sheet Structure= thin sheet cleavage

## Slide 26: Silicates Formation
Most Silicate minerals for as molten rock is cooling “Crystalization”.
Cooling may occur near the at or near the Earth’s surface (low temp. & pressure) or at great depth (high temp. & pressure).
The Environment during crystallization and the chemical composition of the molten rock determine the type of mineral produced.
Ex: Olivine crystallizes at high temp., while Quartz at low temp.
Some silicate minerals may even form from the weathering of older minerals on the surface. Others under extreme pressures during mountain building.
In Conclusion, each silicate mineral has a structure & chemical composition that indicate the conditions of its formation.

## Slide 27: Formation of Minerals: Bowen’s Reaction Series
Bowe’s experiments in the lab showed that:
All magma components cool at 200ᵒc.
Minerals in magma cool (i.e. crystallize/ form) in a systematic manner, based on their melting points.
Ultramafic Mafic or Basaltic  Intermediate or Andesitic  Felsic or Granitic.
Olivine Biotite K-Feldspar Muscovite  Quartz

## Slide 28: Bowen’s Reaction Series showing the sequence in which minerals crytallize from a magma

## Slide 29: Silicate Groups: Light Silicates
Silicates are divided into two major groups based on chemical composition.
A) The Light Silicates “non-ferromagnesian”:
They are light in color & a specific gravity of 2.7, which is attributed to the limited amount of iron & magnesium. Instead they contain varying amounts of Al, K, Ca, & Na.
Feldspar Group: the most abundant, partially due to the wide range of temperatures & pressures they can form at. The are hard (6 on Mohs Scale), have glassy to pearly luster, & cleavage along 2 planes at 90ᵒ.
Types of Feldspar/ Properties | K- Feldspar (Orthoclase) | Plagioclase Feldspar
Chemical comp. | Contains K | Contains Na, Ca
Color | Light cream to salmon pink | White to medium grey
Striations (multitude of parallel lines on cleavage) | NO | YES

## Slide 30: Silicate Groups: Light Silicates
The Light Silicates “non-ferromagnesian” (continued):
Quartz: Entirely made of SiO2, hence called “silica”. It is hard (7 on Mohs scale), so it is resistant to weathering. Its has no cleavage, but rather when broken goes through conchoidal fracture.
When pure & without interferance, quartz forms hexagonal crystals with pyramid- shaped ends.
Muscovite: A common member of the mica family. Has a light color and is pearly in luster. It is very shiny so it can be identified by the sparkle it gives to rocks (like glitter).
Clay Minerals: A range of complex minerals,
like mica, that have sheet stuctures.
Unlike other common silicates, they form
on the surface as a result of chemical
weathering (making up a large % of soil).
Muscovite

## Slide 31: Silicate Groups: Heavy Silicates
B) The Dark Silicates “ferromagnesian”:
As the name implies, they are dark and they contain iron “ferro” & magnesium “magnesian” in their structure. This makes them heavy, with a specific gravity of 3.2-3.6.
Olivine Group: A family of high-temp. silicate minerals that are black to olive green in color and typically forms small granular crystals. Has a glassy luster, conchoidal fractures (single tertrahedron).
Pyroxene Group: Most common member is Augite, a black mineral with 2 cleavage planes meeting at nearly 90 degrees (single chain).
It is the dominant mineral in basalt.

## Slide 32: Silicate Groups: Heavy Silicates
B) The Dark Silicates “ferromagnesian” (contined):
Amphibole Group: Hornblende is the most common member, which is dark green to black, has 2 cleavage planes at 60 & 120 degrees, has similar appearance to Augite, & is found in igneous rocks.
Biotite: A dark iron-rich member of the mica. It has a sheet structure that gives it an excellent cleavage in one direction. Its dark shiny appearance help distinguish it from other dark silicates. It is common in igneous rocks like granite.

## Slide 33: Important Non-Silicate Minerals
Carbonates:
Composed of the carbonate ion (CO3¯²).
The two most common carbonates are calcite (CaCO3) and dolomite (CaMg(CO3)2). They both have glassy luster & a hardness of 3-4.
They are hard to tell apart, but a way is to use dilute hydrochloric acid; calcite reacts very quickly (fizzes!) while dolomite reacts much slower.
When they are the dominant mineral, calcite forms the rock “limestone” and dolomite “dolostone”, two very common sedimentary rocks.
Limestone has many uses including in Palestine: road aggregate, as building stone, & as the main ingredient in portland cement.

## Slide 34: Other Non silicates
Halides: nonsilicates minerals frequently found in sedimentary rocks (ex: halite or salt NaCl).
Oxides (O¯²)
Sulfides (S¯²)
Sulfates (SO4¯²): ex: Gypsum used in plaster.
Native Elements (such as gold, silver, diamond, etc.)