## Slide 1: Subdivision project
Introduction :
What is the project ?
the objective of the project
What we do in the project ?

## Slide 3
Roads
Main road 25 m
Road 12 m
Road 14 m

## Slide 4
Slope for Roads
Maximum slope 10.6%
Slopes 6% or less are recommended on most roads but exceptions of up to 12%

## Slide 6
Cul-de-sac

## Slide 7: Zoning :

## Slide 8: Zones :
We have many zones:
Zone A
Zone B
Zone C
Zone D
Public zones

## Slide 9: Parcels:
We have 4 types of parcels:
Parcel A
Parcel B
Parcel C
Parcel D

## Slide 10: Parcels A :
500 – 600 sq. meters .
Minimum frontage distance 20m.
no limitations on number of parcels. (238)

## Slide 11: Parcels B (villas) :
900 – 1100 sq. meters residential.
Minimum frottage distance 25 m.
the number of parcels should be (10% - 20%) of the number of parcels A area . (12.5)

## Slide 12: Parcels C (commercial) :
2000 – 3000 sq. meters.
Minimum frontage distance 25 meters.
Number of parcels must be in the range of 3-10. (9) .
Minimum setbacks are front: 18 meters, back and sides 4 meters.
Parking (20).

## Slide 13: Parcels D :
1500-3000 sq. meters.
Number of parcels must be in the range of 2-4.
Minimum frontage distance 15 meters.
minimum setbacks: front 10 meters, sides and back 5 meters.
apartments with 6-8 floors .

## Slide 14: Public zones :
We have 5 public area:
Playground and garden
clinic
mosque
school

## Slide 15: Cross sections

## Slide 16: Road cross section elements
Road width
Roadway width
Median
Shoulder
Parking lanes
sidewalks

## Slide 17: Main Road
Two way, two lanes in each direction Roadway width: 3.7m
Parking: 2m
Shoulder:1.6m
Median: 3m (U-turn, Left turn, safety)

## Slide 18: Other roads: (12m, 14m)
Two way, one lane in each direction
Roadway width ( 2.75-3 m)
2m lane in each direction ( parking)
1.25m lane in each direction (sidewalk)
2m median

## Slide 19: Vertical Alignment for main road 20m stations
Total cut volume | Total fill volume
102.16 m^3 | 468.01 m^3

## Slide 20: Re parceling of area

## Slide 21: parcels before planning

## Slide 23: Agriculture road

## Slide 24: After planning

## Slide 29: Parcels before planning parcels after planning